## Slide 1: Shale oil extraction and CO2 sequestration by a novel method of hot gas injection
Michael Youtsos – Energy Group
Cambridge University Engineering Department
Supervisor: Prof. Nondas Mastorakos
Notes: Hello, my name is Michael Youtsos and today I want to talk to you about injecting hot CO2 into underground reservoirs and how by doing that we can extract what’s known as Shale Oil

## Slide 2: What is Shale Oil?
Shale rock contains organic material called Kerogen
When you heat it, Kerogen decomposes to Oil and Gas
There are about 2 - 4 trillion barrels worth of shale oil in the USA alone . . 400 years of oil supply!!
O(10-6m)
Notes: SO FIRST I WOUL HAVE TO TELL YOU THAT SHALE ROCK, WHICH STORES SHALE GAS BTW, . . . .

## Slide 3: Reaction Mechanism [Burnham and Braun (1991)]
Kerogen + Energy Heavy Oil + Light Oil + Gas + Char
Heavy Oil + Energy  Light Oil + Gas + Char
Light Oil, Gas and Solid residue decomposition reactions…
543 K
643K
Notes: So how does Kerogen become oiL? There is no one agreed upon mechanism!

## Slide 4: Novel (simple) Extraction Technique
Inject hot, pressurized CO2 to heat shale underground (in situ heating)
Current inefficiencies of extraction have a lot to do with
  Large timescales for extraction due to conduction heating (3 – 5 years) [Fan et al. (2009), White et al. (2010)]
  Inefficient thermal waves due to conduction heating (Low EROI)
  Huge environmental costs (Retorting of Shale) [Brandt (2008)]
Gas injection may solve these issues:
  As a fluid it will travel relatively quickly through the reservoir
  It will carry the thermal wave with it [Jupp & Woods (2003)]
  It can be sequestered directly underground after heating
Notes: So, what are we trying to contribute with this research?
And the reason we are trying to do that is . . . Current inneficies are mostly due to conduction heating: takes to long, wastes energy due to it’s thermal wave’s long tail and therefore v. env costly also!!

## Slide 5: Governing equations [Chen et al. (2006)]
Multiphase flow in a reservoir: Oil and Gas
Darcy’s Law to find phase velocities – (each phase)
Mass conservation – (each phase)
Notes: Now how to physically describe these underground processes?

## Slide 6: Governing equations [Woods & Jupp (2003)]
Dynamic Pressure Equation – (liquid phases)
Reservoir Energy/Temperature equation – (all phases)
Ratio of specific heat capacity of fluids to that of solids
Notes: Next we consider that these phases exist together on a microscopic grain level underground
Heat transfer rate on a grain level is so fast that we can assume that we have one energy equation

## Slide 7: Problem Description
1D Cylindrical coordinates
Injected CO2: 230 bar, 573K
Reservoir: Porosity = 0.1, Permeability = 5mD,
Richness = 30 gal/ton, Pressure = 100 bar
Notes: And this is what our problem now looks like
A 1D grid, discretized in cylindrical coordinates
Medium richness about 500 m undergroun! --- B/C;s and IC’s are our base case

## Slide 8: Numerical Method
Discretized PDE’s and fed them as ODE’s to DVODPK
Second order upwind differencing for advection terms
Second order centered differencing for diffusion terms
Notes: So we take our discretized PDES, which we have discretized as below, and feed them to the ODE solver DVODPK

## Slide 9: Base Case – 20 days of heating

## Slide 10: Base Case – 20 days of heating
Steep thermal profiles for gas injection (LEFT)
Long thermal tails for conduction (RIGHT)
Notes: BUT THE INTERESTING STUFF IS OVER HERE

## Slide 11: Base Case – 20 days of heating
Non dimensional flux of oil (LEFT) peaks at thermal wave front
[ Thermal wave speed ] / [ Fluid speed ] (RIGHT) minimum follows reaction / thermal front
Notes: AND THERE”S A LOT TO UNDERSTAND FROM PLOTTING THESE TWO NON DIMENSIONAL VARIABLES AGAINST A NON DIMENSION COORDINATE ETA, WHICH MOVES WITH THE THERMAL WAVE
THERMAL AND REACTION FRONT ARE FOLLOWING EACH OTHER VERY CLOSELY - THERMAL WAVE SPEED IS NOT AFFECTED DOWNSTREAM, STAYS WITHIN REACTION WAVE

## Slide 12: Temperature variations
Very high temperatures form strong convective wave
Lead to rapid heavy oil decomposition
Notes: WHAT HAPPENS WHEN UP THE TEMP?? BETTER WAVE, TOO MUCH DECOMP
TOO LOW A TEMP, and NO DECOM
EFFICIENCY GRAPHS TELL THAT STORY AS WELL

## Slide 13: Pressure variations
High pressures lead to quick extraction of oil but require high energy injection rates
Notes: ON THE OTHER SIDE OF THINGS
BUT, AS THIS GRAPH SHOWS, IT WONT OFFSET THE EXTRA AMOUNT OF ENERGY THAT YOU WILL HAVE TO PUMP IN!

## Slide 14: Thermal conduction vs. Gas injection
Efficiency graph: injection is more efficient (EROI 6:1), extracts oil quicker.
Notes: SO FINALLY, here we are

## Slide 15: Future Work
 Performing a more detailed Sensitivity Analysis
Lattice Boltzmann method to explore interaction of shale products on a molecular level
In situ combustion of organic solid residue to produce CO2 for heating other deposits

## Slide 16: Thank you very much! Questions?
Burnham and Braun (1991)
Chen et al. (2006)
Fan et al. (2009)
White et al. (2010)
Woods & Jupp (2003)
Bibliography:

## Slide 17: Closure Models [White et al. (2010), Chen et al. (2006)]
Permeability = function( pore pressure, solid content )
Porosity = function( pore pressure )
Relative permeability = function ( volume saturation of oil)
Notes: easure of the ability of a porous material (often, a rock or unconsolidated material) to allow fluids to pass through it.
In multiphase flow in porous media, the relative permeability of a phase is a dimensionless measure of the effective permeability of that phase. It is the ratio of the effective permeability of that phase to the absolute permeability